## Slide 1: Summary of Initial dredged material placement operations at north head site (NHS) & evaluation of bathymetry response
An Interim Progress Report to MCR Stakeholders
Astoria, Oregon
Portland District
7 DEC 2018

## Slide 2
Review of Intended Concept: Presented in MAY 2018

## Slide 3
Review of Intended Concept: Presented in MAY 2018

## Slide 4
NORTH HEAD STUDY AREA
Pacific
Ocean
Mouth of Columbia River
North Head
Benson Beach
Peacock Spit

## Slide 7
19-21 SEP 2018
Hopper Dredge Tracklines
During Placement Operations
9 loads placed along
prescribed 150-ft wide transect zone
150 ft wide
transect zone

## Slide 8
FULL Hopper Load (5000 CY)
EMPTY Hopper Load (0 CY)
START Dump
END Dump
23 min
21 min
18 min
23 min
17 min
18 min
22 min
20 min
19 min

## Slide 9
20 AUG 2018
30 days BEFORE initial placement
-46 ft MLLW
-51 ft MLLW
-41 ft MLLW

## Slide 10
21 SEP 2018
0 day AFTER placement
9 loads placed during 19-20 SEP = 51,000 CY
by hopper dredge Essayons (~5,500 cy/load)
material = fine-medium sand dredged from
MCR-FNC (dia=0.15 – 0.35 mm)
-46 ft MLLW
-51 ft MLLW
-41 ft MLLW

## Slide 11
27 SEP 2018
7 days AFTER placement
-46 ft MLLW
-51 ft MLLW
-41 ft MLLW

## Slide 12
11 OCT 2018
22 days AFTER placement
-46 ft MLLW
-51 ft MLLW
-41 ft MLLW

## Slide 13
20 NOV 2018
61 days AFTER placement
-46 ft MLLW
-51 ft MLLW
-41 ft MLLW
17 Kcy on Seabed within “mound” feature
32 Kcy eroded off of mound feature
during 21 SEP – 20 NOV

## Slide 14
Survey Difference 20 AUG-21 SEP 2018
0 day AFTER placement - 51,000 CY placed
49 Kcy on Seabed within “mound” feature
Max mound height = 1.9 ft with respect to 20 AUG seabed
Deposition, ft

## Slide 15
Survey Difference 20 AUG-27 SEP 2018
37 Kcy on Seabed within “mound” feature
12 Kcy eroded off of mound feature
during 21 SEP – 27 SEP
Max mound height = 1.5 ft with respect to 20 AUG seabed
7 days AFTER placement - 51,000 CY initially placed
Deposition, ft

## Slide 16
Survey Difference 20 AUG-11 OCT 2018
46 Kcy on Seabed within “mound” feature
9 Kcy deposited on bathymetry
during 27 SEP – 11 OCT
1 Kcy net erosion from 21 SEP
Max mound height = 1.5 ft with respect to 20 AUG seabed
22 days AFTER placement - 51,000 CY initially placed
Deposition, ft

## Slide 17
Survey Difference 20 AUG-20 NOV 2018
17 Kcy on Seabed within “mound” feature
29 Kcy eroded off mound feature
during 11 OCT – 20 NOV
32 Kcy net erosion from 21 SEP
Max mound height = 1.0 ft with respect to 20 AUG seabed
61 days AFTER placement - 51,000 CY initially placed
Deposition, ft

## Slide 18
NHS
Placement
21-SEP
survey
27-SEP
survey
11-OCT
survey
20-NOV
survey
SURFACE CURRENTS

## Slide 19
Significant bottom
transport

## Slide 20
Currents > 2 ft/sec can mobilize fine-medium sand

## Slide 21
NHS-Interim Findings
9 loads (51,000 cy) of sand where placed by the gvt hopper dredge Essayons along a 5,000 ft-long transect, using thin-layer placement method, and produced a 2 ft high mound. The mound was 5,000 ft long and 300 to 500 ft wide. All 9 loads were released within the 150 ft wide placement transect.
Placement occurred during 19-21 SEP 2018, in water depth of 40-50 ft depth along the northern flank of Peacock Spit.
Post-placement surveys were conducted at 0 days, 7 days, 22 days, and 60 days after placemnt completion.
At day 0, the initial detectable volume of placed material along the mound feature was 49,000 CY (2,000 cy of dredged material was dispersed to the surrounding seabed during placement). By day 7, the detectable mound volume had been reduce to 37,000 cy due to sediment dispersion (12,000 cy dispersed from mound). Waves were 3-10 ft high, 6-10 sec, and S-NW.
At day 22, 9,000 cy of sediment had been re-deposited onto the mound area by waves and currents stirring sediment on Peacock Spit (waves were 3-12 ft high, 6-18 sec, and S-NW).
By day 60, the mound volume had been reduced to 17,000 CY (loss of 32,000 cy since day 0). Max mound height was 1 ft.

## Slide 22
20 AUG 2018
21 SEP 2018
27 SEP 2018
11 OCT 2018
20 NOV 2018
20 AUG 2018

## Slide 23
20 AUG-21 SEP 2018 1.7 ft
20 AUG-27 SEP 2018 1.5 ft
20 AUG-11 OCT 2018 1.5 ft
20 AUG-20 NOV 2018 1.0 ft
17 Kcy on Seabed
32 Kcy eroded
49 Kcy on Seabed

## Slide 25
The Health of Benson Beach appears to be related to how much dredged material we place at SWS.
The less placed at SWS, the more
erosion occurs along Benson Beach.